GPS-SDR

Interface Specification

Revision 1.0

December 5, 2008

Revision History

Revision/Change Record
Revision	Date	Description	Pages Affected
1	12/05/08	Initial Release	All

# Introduction

This document describes the command and telemetry interface for the gps-sdr receiver. Users may use the provided GUI (gps-gui) to control the receiver in an interactive manner, or can use the information in this document to directly apply commands to the receiver over a named pipe or RS-232 interface.

# GPS-SDR Command Arguments

The following descriptions can be accessed by typing “gps-sdr –help” at the command line:

usage: [-p] [-c] [-l] [-d] [-g] [-v] [-n] [-gui] [-ser] [-w] [-u]
[-p] <filename> use prerecorded data
[-c] log high rate channel data
[-l] log navigation data
[-d] <N> decimate logged nav data by this N factor
[-g] log google earth data
[-v] be verbose
[-n] ncurses OFF
[-gui] run receiver with the GUI app over a named pipe
[-ser] run receiver with the GUI app over a serial port
[-w] start receiver in warm start, using almanac and last good position
[-u] run receiver with usrp-gps as child process

# GPS-SDR Physical Interfaces

The gps-sdr is able to utilize two interfaces, a named pipe interface for control on the same computer that the receiver is running, or over a RS-232 serial connection. Only one may be used at any given time. The named pipe (NP) interface provides more flexibility, mainly because it is not bandwidth limited. The RS-232 connection operates at 115200 bps, limiting the telemetry bandwidth to ~14 kB/s.

The named pipe interface is composed of two Linux named pipes, one for sending commands to the receiver, and the other for the receiver's output:

Receiver input:	/tmp/GUI2GPS
Receiver output:	/tmp/GPS2GUI

To start the receiver using this interface run the following command:

gps-sdr -gui

The receiver, by default, will send data out at a rate of 10 Hz. This can be lowered by using the “-d” command argument on startup. Use the “-d” argument in the following manner:

[-d] <N> decimate logged nav data by this N factor

Note N should be a factor of the #define TICS_PER_SECOND found in config.h. By default TICS_PER_SECOND == 10, hence N can be 1, 2, 4, 5, or 10.

By default gps-sdr will use the RS-232 interface mapped to /dev/ttyS0. The serial configuration is the following:

Baud	115200
Parity	None
Stop Bits	1
Data Bits	8
Flow Control	None

Note that the user should limit the telemetry to 1 Hz, so the flag “-d 10” should be used in conjunction with “-ser”. To start the receiver in serial mode, use the command:

gps-sdr -ser -d 10

# Packets

GPS-SDR uses packet headers, defined by the Consultative Committee for Space Data Systems (CCSDS), for both the command and telemetry packets. Each packet, composed of the preamble, header, and payload, will be limited to 512 bytes TOTAL. Larger messages and commands will be broken into subpackets, with the appropriate CCSDS header configuration. The CCSDS packet header description can be found at:

http://public.ccsds.org/publications/archive/133x0b1.pdf

The packet format is illustrated below:

Figure 1: Packet Format

The preamble will always be 0xAAAAAAAA (alternating 1's and 0's). The packet version number, as recommended in CCSDS 133.0-B-1, will be '000'. The packet type will be '0' for messages, and '1' for commands. The secondary header flag will always be '0', given that the secondary CCSDS header will NOT be used.

The sequence flag will follow the format described in CCSDS 133.0-B-1 to indicate messages and/pr commands broken over multiple packets. The sequence count will contain the least significant 14 bits of the receiver's internal count of the number of packets it has emitted. The packet length will contain the number of bytes in the payload. Given the packet's size limit of 512 bytes, this value can be as large as 496 bytes. The payload will be filled with a structure corresponding to the application process identifier (APID). The mnemonics linking APID, enum, structure, and variable are as follows:

Enum	NAME_M_ID or NAME_C_ID
Structure	Name_M or NAME_C
Variable	name

All commands and structures must be 4 byte aligned. Note, as a rule, command and telemetry structures will only use the following types for data members:

Type	Description
int32	32 bit signed integer
uint32	32 bit unsigned integer
float	32 bit floating point
double	64 bit floating point

Smaller values (8 or 16 bit) may be accessed by explicit packing and unpacking of the data members. Any data members that are packed will be described in this document.

# Commands
## Overview
Commands will be packetized according to the format described above. Each command will have an associated structure that will compose the payload of the packet. These structures can be found in Appendix 1 of this document. If the command payload exceeds 496 bytes it will be broken over multiple packets. Additionally, the receiver will acknowledge each command by echoing the value found in the packet sequence count value of the CCSDS header. If the command is broken over multiple packets, then the echoed value will be the first packet sequence count of the given command.

## Command APID Map

Command	Application Process Identifier
RESET_RESET_C_ID	1
RESET_PVT_C_ID	2
RESET_EKF_C_ID	3
RESET_CHANNEL_C_ID	4
RESET_EPHEMERIS_C_ID	5
RESET_ALMANAC_C_ID	6
SET_PVT_C_ID	7
SET_ALMANAC_C_ID	8
SET_EPHEMERIS_C_ID	9
SET_ACQ_CONFIG_C_ID	10
GET_MEASUREMENT_C_ID	11
GET_PSEUDORANGE_C_ID	12
GET_ALMANAC_C_ID	13
GET_EPHEMERIS_C_ID	14
GET_ACQ_CONFIG_C_ID	15
GET_SV_PREDICTION_C_ID	16
GET_EPHEMERIS_VALID_C_ID	17
GET_BOARD_HEALTH_C_ID	18
GET_ACQ_COMMAND_C_ID	19
GET_SV_POSITION_C_ID	20
GET_CHANNEL_C_ID	21

## Command Descriptors
### RESET_RESET_C_ID
This command clears all GPS related information from the receiver. The PVT, EKF, ephemerides, almanac, and all tracking channels are reset to their initial states.
### RESET_PVT_C_ID
This command resets the receiver's single point position (SPS) to the center of the earth, and erases all knowledge of GPS time. The argument flag is not used.

### RESET_EKF_C_ID
This command resets the receiver's extend Kalman filter (EKF) state to the center of the earth, and erases all knowledge of GPS time within the EKF. Note the EKF will not reinitialize until the receiver produces 60 consecutive valid PVT solutions. The argument flag is not used.

### RESET_CHANNEL_C_ID
This command forces the receiver dump the given tracking channel. This command can be useful if a cross correlation is detected by the user but the receiver has not rejected it. Note that the argument chan is zero indexed. If chan < 0 || chan >= MAX_CHANNELS the receiver will dump ALL the channels.

### RESET_EPHEMERIS_C_ID
The command will cause the receiver to erase knowledge of the given SV's decoded ephemeris. If sv < 0 || sv >= NUM_CODES, then all ephemerides will be erased.

### RESET_ALMANAC_C_ID
The command will cause the receiver to erase knowledge of the given SV's decoded almanac. If sv < 0 || sv >= NUM_CODES, then all almanacs will be erased.

### SET_ALMANAC_C_ID
This command allows external loading of the almanac. The command will simply copy the Almanac_M held in almanac to the SV enumerated in the argument sv. Note that if
sv < 0 || sv >= NUM_CODES the command will be ignored.

### SET_EPHEMERIS_C_ID
This command allows the external loading of the ephemerides. The command will simply copy the Ephemeris_M held in ephemeris to the SV enumerated in the argument sv. Note that if
sv < 0 || sv >= NUM_CODES the command will be ignored.
### GET_MEASUREMENT_C_ID
This command will cause the receiver to continuously emit raw measurements for all channels. Set flag to '1' to turn streaming on, '0' for off.

### GET_PSEUDORANGE_C_ID
This command will cause the receiver to continuously emit pseudoranges for all channels. Set flag to '1' to turn streaming on, '0' for off.

### GET_EPHEMERIS_C_ID
This will cause the receiver to emit the given SV's decoded ephemeris once.
If sv < 0 || sv >= NUM_CODES then all ephemerides will be emitted.

### GET_ALMANAC_C_ID
This will cause the receiver to emit the given SV's decoded almanac once.
If sv < 0 || sv >= NUM_CODES then all almanacs will be emitted.

### GET_ACQ_CONFIG_C_ID
Instructs the receiver to emit the acquisition configuration.

### GET_SV_PREDICTION_C_ID
Instructs the receiver to emit the predicted state of the given SV based on the GPS almanac. If sv < 0 || sv >= NUM_CODES the receiver will emit the most recent predictions for all the SVs.

### GET_EPHEMERIS_VALID_C_ID
Emit the ephemeris and almanac validity message, Ephemeris_Valid_M.

### GET_BOARD_HEALTH_C_ID
Emit the board health message Board_Health_M.

### GET_ACQ_COMMAND_C_ID
Emit the acquisition command and result for the given SV. If sv < 0 || sv >= NUM_CODES the receiver will emit predictions for all the SVs.

### GET_SV_POSITION_C_ID
This command will cause the receiver to continuously emit sv positions for all channels. Set flag to '1' to turn streaming on, '0' for off.

### SET_ACQ_CONFIG_C_ID
This command allows the user to customize the acquisition process. The min_doppler and max_doppler arguments define the upper and lower bounds of the Doppler search space. Note that if these lie outside the #define MAX_DOPPLER found in config.h they will be set to MAX_DOPPLER. The doppler_range argument defines the Doppler search space, plus-minus, to search over if the receiver has state information and the almanac is decoded for the given SV (i.e. a warm acquisition).

The last three arguments allow control of the strong, medium, and weak acquisition modes. A value of '0' turns the particular mode off completely. A value of '1' turns the mode on for both cold and warm acquisitions. Finally a value of '2' allows the receiver to search in the given mode only for a warm acquisition.

### SET_PVT_C_ID
This command initializes the receiver's PVT solution with the included state information. If the receiver also has a current almanac this enables a narrowing of the search space and facilitates faster acquisition of signals.

# Messages
## Overview
Messages are one of three types: fixed, requestable, and streaming.

Fixed messages will be emitted by the receiver after each PVT solution generation. Fixed messages CANNOT be turned off.

Requestable messages will be emitted by the receiver only after receiver is given a command to do so. They will be emitted only once for each command received.

Streaming messages have the ability to be turned on and off as required. These messages are typically data that can be used to debug the internal workings of the receiver. If activated, these messages will be emitted at the same rate as the periodic messages, i.e. once per PVT solution.

Finally, the COMMAND_ACK_M_ID is a special case. This message is only emitted upon the reception and execution of a command.

## Message APID & Type Map

Command	Application Process Identifier	Type
TASK_HEALTH_M_ID	1	Fixed
SPS_M_ID	2	Fixed
CLOCK_M_ID	3	Fixed
EKF_M_ID	4	Fixed
MEASUREMENT_M_ID	5	Streaming
PSEUDORANGE_M_ID	6	Streaming
SV_POSITION_M_ID	7	Streaming
CHANNEL_M_ID	8	Streaming
BOARD_HEALTH_M_ID	9	Request
ACQ_CONFIG_M_ID	10	Request
EPHEMERIS_M_ID	11	Request
ALMANAC_M_ID	12	Request
EPHEMERIS_VALID_M_ID	13	Request
SV_PREDICTION_M_ID	14	Request
ACQ_COMMAND_M_ID	15	Request
COMMAND_ACK_M_ID	16	N/A
	17
	18
	19
	20
	21
	22
	23
	24
	25
	26
	27

## Message Descriptors
### TASK_HEALTH_M_ID
This message contains the execution counters, OS start tic, and OS stop tic of each thread's main body of code. The least significant bit of the start and stop tics correspond to a 10 millisecond duration. The tasks will be identified by the enum TASK_IDS found in config.h.

### SPS_M_ID
The single point solution (SPS) message is the main output of the receiver. It gives the receiver's estimated position, velocity, acceleration, and time based on the least squares algorithm. The SPS will be updated only when >4 SVs are being concurrently tracked.

### CLOCK_M_ID
The clock message gives more detailed information concerning the receiver's estimate of time, based on the least squares PVT.
### CHANNEL_M_ID
The channel message gives detailed insight into the status of each tracking channel.

### SV_POSITION_M_ID
The SV position message gives information on the calculated SV position based on the GPS ephemeris. This position will correspond to the time of transmission, per IS-GPS-200D. The SV position will be updated each time the receiver computes a least squares PVT solution.

### EKF_M_ID
Currently the extended Kalman filter does not exist in the receiver, this structure will change when it is added.

### MEASUREMENT_M_ID
The measurement message gives the raw correlator state taken at each measurement tic. This measurement is turned into a pseudorange in the PVT thread.

### PSEUDORANGE_M_ID
The pseudorange message contains the raw pseudorange calculated by the receiver when forming the PVT solution.

### BOARD_HEALTH_M_ID
This message provides status and health concerning the receiver's hardware, including portions of the RF card, power supply voltages, thermistor readings, and FPGA version registers.

### EPHEMERIS_M_ID
The decoded ephemeris, read IS-GPS-200D for more specific information.

### ALMANAC_M_ID
The decoded almanac, read IS-GPS-200D for more specific information.

### EPHEMERIS_VALID_M_ID
Provides insight into the status of the Ephemeris object, indicating which ephemerides and almanacs have been decoded.

### COMMAND_ACK_M_ID
This message will be sent upon completion of each command sent to the receiver. The command_status will indicate success or a rejection of the command.

### SV_PREDICTION_M_ID
The predicted state of the given SV. This information is updated in the SV_Select thread using the PVT's output and the almanac.

### ACQ_COMMAND_M_ID
This message gives insight into the acquisition engine's most recent acquisition attempt.

# Appendix 1: Command Structures

/*! \ingroup COMMANDS
Dump everything (PVT/Ephemeris/Almanac/Channels/EKF)
*/
typedef struct Reset_Reset_C
{
int32 flag;	//!< Flag for no reason
} Reset_Reset_C;

/*! \ingroup COMMANDS
Reset the PVT
*/
typedef struct Reset_PVT_C
{
int32 flag;	//!< Flag for no reason
} Reset_PVT_C;

/*! \ingroup COMMANDS
Reset the EKF
*/
typedef struct Reset_EKF_C
{
int32 flag;	//!< Flag for no reason
} Reset_EKF_C;

/*! \ingroup COMMANDS
Dump the desired channel
*/
typedef struct Reset_Channel_C
{
int32 chan;	//!< Channel #, or all if chan >= MAX_CHANNELS
} Reset_Channel_C;

/*! \ingroup COMMANDS
Clear the given ephemeris
*/
typedef struct Reset_Ephemeris_C
{
int32 sv;	//!< SV #, or all if sv >= NUM_CODES
} Reset_Ephemeris_C;

/*! \ingroup COMMANDS
Clear the given almanac
*/
typedef struct Reset_Almanac_C
{
int32 sv;	//!< SV #, or all if sv >= NUM_CODES
} Reset_Almanac_C;

/*! \ingroup COMMANDS
Get a raw measurement
*/
typedef struct Get_Measurement_C
{
int32 flag;	//!< On/off
} Get_Measurement_C;

/*! \ingroup COMMANDS
Get a pseudorange
*/
typedef struct Get_Pseudorange_C
{
int32 flag;	//!< On/off
} Get_Pseudorange_C;

/*! \ingroup COMMANDS
Emit the given ephemerides
*/
typedef struct Get_Ephemeris_C
{
int32 sv;	//!< SV #, or all if sv >= NUM_CODES || sv < 0
} Get_Ephemeris_C;

/*! \ingroup COMMANDS
Emit the given almanac
*/
typedef struct Get_Almanac_C
{
int32 sv;	//!< SV #, or all if sv >= NUM_CODES || sv < 0
} Get_Almanac_C;

/*! \ingroup COMMANDS
Stuff the given almanac
*/
typedef struct Set_Almanac_C
{
int32 sv;	//!< SV #
Almanac_M almanac;	//!< Data to load
} Set_Almanac_C;

/*! \ingroup COMMANDS
Stuff the given ephemeris
*/
typedef struct Set_Ephemeris_C
{
int32 sv;	//!< SV #
Ephemeris_M ephemeris;	//!< Data to load
} Set_Ephemeris_C;

/*! \ingroup COMMANDS
Configure the acquisition
*/
typedef struct Set_Acq_Config_C
{
Acq_Config_M acq_config;
} Set_Acq_Config_C;

/*! \ingroup COMMANDS
Do a warm start.
*/
typedef struct Set_PVT_C
{
double x;	//!< ECEF X position (meters)
double y;	//!< ECEF Y position (meters)
double z;	//!< ECEF Z position (meters)
double vx;	//!< ECEF X velocity (meters/second)
double vy;	//!< ECEF Y velocity (meters/second)
double vz;	//!< ECEF Z velocity (meters/second)
double second;	//!< GPS second
double week;	//!< GPS week
} Set_PVT_C;

/*! \ingroup COMMANDS
Emit an acquisition config message.
*/
typedef struct Get_Acq_Config_C
{
int32 flag;	//!< Not used
} Get_Acq_Config_C;

/*! \ingroup COMMANDS
Emit a SV prediction from SV_Select
*/
typedef struct Get_SV_Prediction_C
{
int32 sv;	//!< SV $
} Get_SV_Prediction_C;

/*! \ingroup COMMANDS
Emit ephemeris/acquisition decode status
*/
typedef struct Get_Ephemeris_Valid_C
{
int32 flag;	//!< Not used
} Get_Ephemeris_Valid_C;

/*! \ingroup COMMANDS
Emit a board health message
*/
typedef struct Get_Board_Health_C
{
int32 flag;	//!< Not used
} Get_Board_Health_C;

/*! \ingroup COMMANDS
Emit an acquisition result
*/
typedef struct Get_Acq_Command_C
{
int32 sv;	//!< SV #
} Get_Acq_Command_C;

/*! \ingroup COMMANDS
Emit an acquisition result
*/
typedef struct Get_SV_Position_C
{
int32 flag;	//!< On/off
} Get_SV_Position_C;

/*! \ingroup COMMANDS
Emit the channel status
*/
typedef struct Get_Channel_C
{
int32 flag;	//!< On/off
} Get_Channel_C;

# Appendix 2: Message Structures

/*! \ingroup MESSAGES
 * Packet dumped to telemetry and to disk to keep track of each channel
 */
typedef struct Board_Health_M
{

//!< Grab FPGA versions
uint32 trk_version;	//!< Tracking FPGA version
uint32 acq_version;	//!< Acquisition FPGA version

//!< DSA Info
uint32 dsa0;	//!< Current state of DSA 0
uint32 dsa1;	//!< Current state of DSA 1
uint32 dsa2;	//!< Current state of DSA 2
uint32 dsa3;	//!< Current state of DSA 3

//!< Overflows on A/Ds
uint32 ovrflw0;	//!< Overflow counter on A/D 0
uint32 ovrflw1;	//!< Overflow counter on A/D 1
uint32 ovrflw2;	//!< Overflow counter on A/D 2
uint32 ovrflw3;	//!< Overflow counter on A/D 3

//!< LO lock indicator
uint32 lo_locked;	//!< Is the LO locked to the synthesizer

//!< Acquisition SRAM
uint32 sram_bad_mem;	//!< Debug info from Steve's POST
uint32 sram_bad_hi;	//!< Debug info from Steve's POST
uint32 sram_bad_lo;	//!< Debug info from Steve's POST

//!< Missed interrupts
uint32 missed_interrupts;//!< Missed interrupts

//!< Software revision
uint32 software_major;	//!< Major version
uint32 software_minor;	//!< Minor version
uint32 software_postfix;//!< Alpha, beta, or gold

} Board_Health_M;

/*! \ingroup MESSAGES
 * Packet dumped to telemetry and to disk to keep track of each channel
 */
typedef struct Task_Health_M
{

uint32 execution_tic[MAX_TASKS];	//!< Execution counters
uint32 start_tic[MAX_TASKS];	//!< Nucleus tic at function entry
uint32 stop_tic[MAX_TASKS];	//!< Nucleus tic at function exit

} Task_Health_M;

/*! \ingroup MESSAGES
 * Packet dumped to telemetry and to disk to keep track of each channel
 */
typedef struct Channel_M
{

float chan;	//!< The channel number
float state;	//!< channel's state
float sv;	//!< SV/PRN number the channel is tracking
float antenna;	//!< Antenna channel is tracking off of
float len;	//!< acummulation length (1 or 20 ms)
float w;	//!< 3rd order PLL state
float x;	//!< 3rd order PLL state
float z;	//!< 3rd order PLL state
float code_nco;	//!< State of code_nco
float carrier_nco;	//!< State of carrier_nco
float CN0;	//!< CN0 estimate
float p_avg;	//!< Filtered version of I^2+Q^2
float bit_lock;	//!< Bit lock?
float frame_lock;	//!< Frame lock?
float navigate;	//!< Navigate on this channel flag
float count;	//!< Number of accumulations that have been processed
float subframe;	//!< Current subframe number
float best_epoch;	//!< Best estimate of bit edge position

} Channel_M;

/*! \ingroup MESSAGES
Raw PVT navigation solution
*/
typedef struct SPS_M
 {

double x;	//!< ECEF x coordinate (meters)
double y;	//!< ECEF y coordinate (meters)
double z;	//!< ECEF z coordinate (meters)
double vx;	//!< ECEF x velocity (meters/sec)
double vy;	//!< ECEF x velocity (meters/sec)
double vz;	//!< ECEF x velocity (meters/sec)
double ax;	//!< ECEF x acceleration (meters/sec/sec)
double ay;	//!< ECEF x acceleration (meters/sec/sec)
double az;	//!< ECEF x acceleration (meters/sec/sec)

double time;	//!< time in seconds
double clock_bias;	//!< clock bias in seconds
double clock_rate; //!< clock rate in meters/second
double latitude;	//!< latitude in decimal radians
double longitude;	//!< longitude in decimal radians
double altitude;	//!< height in meters

double gdop;	//!< geometric dilution of precision
double pdop;	//!< position dilution of precision
double tdop;	//!< time dilution of precision
double hdop;	//!< hdop diultion of precision
double vdop;	//!< vertical dilution of precision

uint32 nsvs;	//!< This is a mask, not a number
uint32 converged;	//!< declare convergence
uint32 tic;	//!< global_tic associated with this solution

uint32 stale_ticks;	//!< count the number of ticks since the last good sltn
uint32 converged_ticks;	//!< count number of converged ticks
uint32 nav_channels;	//!< count number of SVs used in last PVT estimation
uint32 initial_convergence;	//!< Flag set ONCE if the first convergence has occured

uint32 chanmap[MAX_CHANNELS]; //!< Map of channels->sv

} SPS_M;

/*! \ingroup MESSAGES
Contains the clock state
*/
typedef struct Clock_M
{

double receiver_time;	//!< Elapsed receiver time
double rate;	//!< Clock rate
double bias;	//!< Clock bias
double time0;	//!< Guess of gps second at initialization
double time;	//!< Best estimate of GPStime
double time_raw;	//!< Uncorrected time
double week;	//!< GPS week
uint32 state;	//!< Clock state

} Clock_M;

/*! \ingroup MESSAGES
Contains the SV position used for the PVT solution
*/
typedef struct SV_Position_M
{

double x;	//!< ECEF x coordinate (meters)
double y;	//!< ECEF y coordinate (meters)
double z;	//!< ECEF z coordinate (meters)
double vx;	//!< ECEF x velocity (meters/sec)
double vy;	//!< ECEF x velocity (meters/sec)
double vz;	//!< ECEF x velocity (meters/sec)
double ax;	//!< ECEF x acceleration (meters/sec/sec)
double ay;	//!< ECEF x acceleration (meters/sec/sec)
double az;	//!< ECEF x acceleration (meters/sec/sec)
double elev;	//!< Satellite elevation (radians)
double azim;	//!< Satellite azimuth (radians)
double clock_bias;	//!< SV clock bias (seconds)
double frequency_bias;	//!< SV clock rate bias (seconds/second)
double transit_time;	//!< Time of flight from SV to receiver (seconds)
double time;	//!< Time used in SV position calculation (seconds)
double latitude;	//!< Latitude using WGS-84 ellipsoid in decimal (radians)
double longitude;	//!< Longitude using WGS-84 ellipsoid in decimal (radians)
double altitude;	//!< height (meters)
uint32 chan;	//!< Corresponding channel

} SV_Position_M;

/*! \ingroup MESSAGES
EKF navigation solution
*/
typedef struct EKF_M
 {

double x;	//!< ECEF x coordinate (meters)
double y;	//!< ECEF y coordinate (meters)
double z;	//!< ECEF z coordinate (meters)
double vx;	//!< ECEF x velocity (meters/sec)
double vy;	//!< ECEF x velocity (meters/sec)
double vz;	//!< ECEF x velocity (meters/sec)
double ax;	//!< ECEF x acceleration (meters/sec/sec)
double ay;	//!< ECEF x acceleration (meters/sec/sec)
double az;	//!< ECEF x acceleration (meters/sec/sec)

double time;	//!< time in seconds
double clock_bias;	//!< clock bias in seconds
double clock_rate; //!< clock rate in meters/second
double latitude;	//!< latitude in decimal radians
double longitude;	//!< longitude in decimal radians
double altitude;	//!< height in meters

double gdop;	//!< geometric dilution of precision
double pdop;	//!< position dilution of precision
double tdop;	//!< time dilution of precision
double hdop;	//!< hdop diultion of precision
double vdop;	//!< vertical dilution of precision

uint32 nsvs;	//!< This is a mask, not a number
uint32 converged;	//!< declare convergence
uint32 tic;	//!< global_tic associated with this solution

uint32 stale_ticks;	//!< count the number of tics since the last good sltn
uint32 converged_ticks;	//!< count number of converged tics
uint32 nav_channels;	//!< count number of SVs used in last PVT estimation
uint32 initial_convergence;	//!< Flag set ONCE if the first convergence has occured

uint32 chanmap[MAX_CHANNELS];

} EKF_M;

/*! \ingroup STRUCTS
 * The measurement dumped to the PVT object
 */
typedef struct Measurement_M
{

double	code_time;	//!< The code time
double	code_phase;	//!< Code phase (chips)
double	carrier_phase;	//!< Carrier phase (cycles)
double	carrier_phase_prev;	//!< Carrier phase prev (cycles)
double	carrier_phase_prev_prev;	//!< Carrier phase prev prev (cycles)
double	code_phase_mod;	//!< Code phase (chips), mod 1023
double	carrier_phase_mod;	//!< Carrier phase (cycles), mod 1
double	code_nco;	//!< Code NCO
double	carrier_nco;	//!< Carrier NCO
uint32 _1ms_epoch;	//!< _1ms_epoch
uint32 _20ms_epoch;	//!< _20ms_epoch
uint32	_z_count;	//!< The z count
uint32	navigate;	//!< This has been tagged as a good measurement
uint32	sv;	//!< For this sv
uint32	chan;	//!< For this channel
uint32	count;	//!< Corresponds to this tic

} Measurement_M;

/*! \ingroup MESSAGES
Pseudoranges structure, holds both time and meters
*/
typedef struct Pseudorange_M
{

double gpstime;	//!< Time tag associated with pseudorange
double time;	//!< pseudorange in seconds
double time_rate;	//!< pseudorange rate in sec/sec
double meters;	//!< pseudorange in meters
double meters_rate;	//!< pseudorange rate in meters/sec
double residual;	//!< residual in meters
double rate_residual;	//!< rate residual (m/s)
double time_uncorrected;//!< raw pseudorange measurements
double previous;	//!< from previous step, used for err check
uint32 chan;	//!< For this channel
uint32 count;	//!< Corresponds to this tic

} Pseudorange_M;

/*! \ingroup MESSAGES
Decoded ephemeris struct
*/
typedef struct Ephemeris_M
{
double tgd;	//!< Group delay parameter.
double toc;	//!< Reference time of clock data parameter set.
double af0;	//!< Clock correction polynomial coefficient.
double af1;	//!< Clock correction polynomial coefficient.
double af2;	//!< Clock correction polynomial coefficient.
double crs;	//!< Sine harmonic correction to orbital radius.
double deltan;	//!< Mean motion delta from computed value.
double m0;	//!< Mean anomaly at TOE.
double cuc;	//!< Cosine harmonic correction to orbital radius.
double ecc;	//!< Eccentricity.
double cus;	//!< Sine harmonic corr to argument of latitude.
double sqrta;	//!< Square root of semimajor axis.
double toe;	//!< Reference time of ephemeris data set.
double cic;	//!< Cosine harmonic corr to inclination.
double om0;	//!< Right ascension at TOE.
double cis;	//!< Sine harmonic corr to inclination.
double in0;	//!< Inclination at TOE.
double crc;	//!< Cosine harmonic correction to orbital radius.
double argp;	//!< Argument of perigee at TOE.
double omd;	//!< Rate of right ascension.
double idot;	//!< Rate of inclination.
double a;	//!< Derived qty: a = sqrta**2.
double n0;	//!< Derived qty: n0 = sqrt(GravConstant/(a*a*a)).
double relativistic;	//!< Relativistic correction

uint32 sv;	//!< SV #
uint32 zcount;	//!< zcount?
uint32 toewk;	//!< GPS week corresponding to toe.
uint32 fti;	//!< Fit interval.
uint32 iode;	//!< Issue of data, ephemeris.
uint32 tocwk;	//!< GPS week corresponding to toc.
uint32 valid;	//!< 0=No valid data.
uint32 tofxmission;	//!< Time of subframe 1 transmission, sec of week.
uint32 tow;	//!< Truncated TOW count
uint32 subframe_1_health;	//!< Subframe 1 health code.
uint32 code_on_L2;	//!< Code on L2 flag.
uint32 week_number;	//!< GPS week at time of subframe 1 reception.
uint32 L2pdata;	//!< L2 P data flag.
uint32 ura;	//!< Satellite's URA code.
uint32 iodc;	//!< Issue of data, clock.

} Ephemeris_M;

/*! \ingroup MESSAGES
Decoded almanac struct
*/
typedef struct Almanac_M
{

double ecc;	//!< Eccentricity
double toa;	//!< Time of Almanac
double in0;	//!< Inclination
double omd;	//!< Rate of right ascention
double sqrta;	//!< Sqrt of Semi-Major Axis
double om0;	//!< Longitude of Ascending Node
double argp;	//!< Argument of perigee
double m0;	//!< Mean Anomaly
double af0;	//!< Clock parameter 0
double af1;	//!< Clock parameter 1

uint32 sv;	//!< SV #
uint32 week;	//!< Week number
uint32 decoded;	//!< Has this been decoded yet
uint32 health;	//!< Health code

} Almanac_M;

/*! \ingroup MESSAGES
 *
 */
typedef struct Ephemeris_Status_M
{

uint32 valid[NUM_CODES];	//!< Valid ephemeris
uint32 iode[NUM_CODES];	//!< Corresponding IODE
uint32 avalid[NUM_CODES];	//!< Valid almanac

} Ephemeris_Status_M;

/*! \ingroup MESSAGES
 * Data from the FIFO to the Telemetry
 */
typedef struct FIFO_M
{

uint32 tic;
uint32 count;	//!< Number of 1 ms packets processed
uint32 head;	//!< Head pointer number
uint32 tail;	//!< Tail pointer number
uint32 agc_scale;	//!< Value used for AGC scale
uint32 overflw;	//!< Overflows in last ms
uint32 nactive;	//!< Number of channels to process the measurment packet

} FIFO_M;

/*! \ingroup MESSAGES
 * Informs the acquisition in what mode to perform the next acquisition
 */
typedef struct _Acq_Command_M
{

int32 chan;	//!< Which channel this will be mapped to
int32 sv;	//!< Look for this SV
int32 type;	//!< Type (STRONG/MEDIUM/WEAK)
int32 mindopp;	//!< Minimum Doppler
int32 maxdopp;	//!< Maximum Doppler
int32 antenna;	//!< Antenna number
int32 count;	//!< Packet tag
int32 state;	//!< Request started, IF data collected, request complete
int32 success;	//!< Was the SV detected?
float delay;	//!< Delay in chips
float doppler;	//!< Doppler in Hz
float magnitude;	//!< Magnitude

} Acq_Command_M;

/*! \ingroup MESSAGES
 * The predicted state of an SV via the almanac
 */
typedef struct _SV_Prediction_M
{

int32 sv;	//!< SV number
int32 visible;	//!< Should the SV be visible?
int32 tracked;	//!< Is it being tracked?
float elev;	//!< Predicted elev (degrees)
float azim;	//!< Predicted azim (degrees)
float v_elev;	//!< Elevation of vehicle relative to SV
float v_azim;	//!< Azimuth of vehicle relative to SV
float delay;	//!< Predicted delay (seconds)
float doppler;	//!< Predicted Doppler (Hz)
float doppler_rate;	//!< Predicted Doppler rate (Hz/sec)

} SV_Prediction_M;

/*! \ingroup MESSAGES
Acknowledge processing of command
*/
typedef struct Command_Ack_M
{

uint32 command_id;	//!< ID of command received
uint32 command_tic;	//!< Command sequence count
uint32 command_status;	//!< Status (0 for FAIL, 1 for SUCCESS)

} Command_Ack_M;

/*! \ingroup MESSAGES
Configure acquisition
*/
typedef struct Acq_Config_M
{
int32 min_doppler;	//!< Minimum doppler
int32 max_doppler;	//!< Maximum doppler
int32 doppler_range;	//!< Doppler range to search when almanac is valid
int32 acq_strong;	//!< 0 for off, 1 for on, 2 for on IF almanac is valid
int32 acq_medium;	//!< 0 for off, 1 for on, 2 for on IF almanac is valid
int32 acq_weak;	//!< 0 for off, 1 for on, 2 for on IF almanac is valid
} Acq_Config_M;