GPS-SDR

Interface Specification

Revision 1.0

December 5, 2008

Revision History

Revision/Change Record
Revision	Date	Description	Pages Affected
1	12/05/08	Initial Release	All

# Introduction

This document describes the command and telemetry interface for the gps-sdr receiver. Users may use the provided GUI (gps-gui) to control the receiver in an interactive manner, or can use the information in this document to directly apply commands to the receiver over a named pipe or RS-232 interface.

# GPS-SDR Command Arguments

The following descriptions can be accessed by typing “gps-sdr –help” at the command line:

usage: [-p] [-c] [-l] [-d] [-g] [-v] [-n] [-gui] [-ser] [-w] [-u]
[-p] <filename> use prerecorded data
[-c] log high rate channel data
[-l] log navigation data
[-d] <N> decimate logged nav data by this N factor
[-g] log google earth data
[-v] be verbose
[-n] ncurses OFF
[-gui] run receiver with the GUI app over a named pipe
[-ser] run receiver with the GUI app over a serial port
[-w] start receiver in warm start, using almanac and last good position
[-u] run receiver with usrp-gps as child process

# GPS-SDR Physical Interfaces

The gps-sdr is able to utilize two interfaces, a named pipe interface for control on the same computer that the receiver is running, or over a RS-232 serial connection. Only one may be used at any given time. The named pipe (NP) interface provides more flexibility, mainly because it is not bandwidth limited. The RS-232 connection operates at 115200 bps, limiting the telemetry bandwidth to ~14 kB/s.

The named pipe interface is composed of two Linux named pipes, one for sending commands to the receiver, and the other for the receiver's output:

Receiver input:	/tmp/GUI2GPS
Receiver output:	/tmp/GPS2GUI

To start the receiver using this interface run the following command:

gps-sdr -gui

The receiver, by default, will send data out at a rate of 10 Hz. This can be lowered by using the “-d” command argument on startup. Use the “-d” argument in the following manner:

[-d] <N> decimate logged nav data by this N factor

Note N should be a factor of the #define TICS_PER_SECOND found in config.h. By default TICS_PER_SECOND == 10, hence N can be 1, 2, 4, 5, or 10.

By default gps-sdr will use the RS-232 interface mapped to /dev/ttyS0. The serial configuration is the following:

Baud	115200
Parity	None
Stop Bits	1
Data Bits	8
Flow Control	None

Table 1: Serial Port Configuration

Note that the user should limit the telemetry to 1 Hz, so the flag “-d 10” should be used in conjunction with “-ser”. To start the receiver in serial mode, use the command:

gps-sdr -ser -d 10

# Packets

GPS-SDR uses packet headers, defined by the Consultative Committee for Space Data Systems (CCSDS), for both the command and telemetry packets. Each packet, composed of the preamble, header, and payload, will be limited to 512 bytes TOTAL. Larger messages and commands will be broken into subpackets, with the appropriate CCSDS header configuration. The CCSDS packet header description can be found at:

http://public.ccsds.org/publications/archive/133x0b1.pdf

The packet format is illustrated below:

Figure 1: Packet Format

The preamble will always be 0xAAAAAAAA (alternating 1's and 0's). The packet version number, as recommended in CCSDS 133.0-B-1, will be '000'. The packet type will be '0' for messages, and '1' for commands. At this time, the secondary header flag will be '0', given that the secondary CCSDS header is not used.

The sequence flag will follow the format described in CCSDS 133.0-B-1 to indicate messages and/pr commands broken over multiple packets. The sequence count will contain the least significant 14 bits of the receiver's internal count of the number of packets it has emitted. The packet length will contain the number of bytes in the payload. Given the packet's size limit of 512 bytes, this value can be as large as 496 bytes. The payload will be filled with a structure corresponding to the application process identifier (APID). The mnemonics linking APID, enum, structure, and variable are as follows:

Enum	NAME_M_ID or NAME_C_ID
Structure	Name_M or NAME_C
Variable	name

Table 2: Mnenomics

All commands and structures must be 4 byte aligned. Note, as a rule, command and telemetry structures will only use the following types for data members:

Type	Description
int32	32 bit signed integer
uint32	32 bit unsigned integer
float	32 bit floating point
double	64 bit floating point

Table 3: Message Variable Types

Smaller values (8 or 16 bit) may be accessed by explicit packing and unpacking of the data members. Any data members that are packed will be described in this document.

# Commands
## Overview
Commands will be packetized according to the format described above. Each command will have an associated structure that will compose the payload of the packet. These structures can be found in Appendix 1 of this document. The first value of the telecommand payload will always be a 32 bit value that corresponds to the unique ID of the desired command, these IDs are found in Table 4. The APID of each telecommand packet should be equal to COMMAND_M_ID. If this is not true, the command will be ignored.

Figure 2: Telecommand Format

If the command payload exceeds 492 bytes it will be broken over multiple packets. Commands broken over multiple packets will always include the command ID. The receiver will acknowledge each command by echoing the command ID found in the telecommand payload, along with a command execution count and an execution code for the given command.

## Command ID Map

Command	Command ID
RESET_ALL_C_ID	1
RESET_PVT_C_ID	2
RESET_EKF_C_ID	3
RESET_CHANNEL_C_ID	4
RESET_EPHEMERIS_C_ID	5
RESET_ALMANAC_C_ID	6
SET_PVT_C_ID	7
SET_ALMANAC_C_ID	8
SET_EPHEMERIS_C_ID	9
SET_ACQ_CONFIG_C_ID	10
GET_MEASUREMENT_C_ID	11
GET_PSEUDORANGE_C_ID	12
GET_ALMANAC_C_ID	13
GET_EPHEMERIS_C_ID	14
GET_ACQ_CONFIG_C_ID	15
GET_SV_PREDICTION_C_ID	16
GET_EPHEMERIS_VALID_C_ID	17
GET_BOARD_HEALTH_C_ID	18
GET_ACQ_COMMAND_C_ID	19
GET_SV_POSITION_C_ID	20
GET_CHANNEL_C_ID	21

Table 4: Command ID Values

## Command Descriptors
### RESET_ALL_C_ID
This command clears all GPS related information from the receiver. The PVT, EKF, ephemerides, almanac, and all tracking channels are reset to their initial states.
### RESET_PVT_C_ID
This command resets the receiver's single point position (SPS) to the center of the earth, and erases all knowledge of GPS time. The argument flag is not used.

### RESET_EKF_C_ID
This command resets the receiver's extend Kalman filter (EKF) state to the center of the earth, and erases all knowledge of GPS time within the EKF. Note the EKF will not reinitialize until the receiver produces 60 consecutive valid PVT solutions. The argument flag is not used.

### RESET_CHANNEL_C_ID
This command forces the receiver dump the given tracking channel. This command can be useful if a cross correlation is detected by the user but the receiver has not rejected it. Note that the argument chan is zero indexed. If chan < 0 || chan >= MAX_CHANNELS the receiver will dump ALL the channels.

### RESET_EPHEMERIS_C_ID
The command will cause the receiver to erase knowledge of the given SV's decoded ephemeris. If sv < 0 || sv >= NUM_CODES, then all ephemerides will be erased.

### RESET_ALMANAC_C_ID
The command will cause the receiver to erase knowledge of the given SV's decoded almanac. If sv < 0 || sv >= NUM_CODES, then all almanacs will be erased.

### SET_ALMANAC_C_ID
This command allows external loading of the almanac. The command will simply copy the Almanac_M held in almanac to the SV enumerated in the argument sv. Note that if
sv < 0 || sv >= NUM_CODES the command will be ignored.

### SET_EPHEMERIS_C_ID
This command allows the external loading of the ephemerides. The command will simply copy the Ephemeris_M held in ephemeris to the SV enumerated in the argument sv. Note that if
sv < 0 || sv >= NUM_CODES the command will be ignored.
### GET_MEASUREMENT_C_ID
This command will cause the receiver to continuously emit raw measurements for all channels. Set flag to '1' to turn streaming on, '0' for off.

### GET_PSEUDORANGE_C_ID
This command will cause the receiver to continuously emit pseudoranges for all channels. Set flag to '1' to turn streaming on, '0' for off.

### GET_EPHEMERIS_C_ID
This will cause the receiver to emit the given SV's decoded ephemeris once.
If sv < 0 || sv >= NUM_CODES then all ephemerides will be emitted.

### GET_ALMANAC_C_ID
This will cause the receiver to emit the given SV's decoded almanac once.
If sv < 0 || sv >= NUM_CODES then all almanacs will be emitted.

### GET_ACQ_CONFIG_C_ID
Instructs the receiver to emit the acquisition configuration.

### GET_SV_PREDICTION_C_ID
Instructs the receiver to emit the predicted state of the given SV based on the GPS almanac. If sv < 0 || sv >= NUM_CODES the receiver will emit the most recent predictions for all the SVs.

### GET_EPHEMERIS_VALID_C_ID
Emit the ephemeris and almanac validity message, Ephemeris_Valid_M.

### GET_BOARD_HEALTH_C_ID
Emit the board health message Board_Health_M.

### GET_ACQ_COMMAND_C_ID
Emit the acquisition command and result for the given SV. If sv < 0 || sv >= NUM_CODES the receiver will emit predictions for all the SVs.

### GET_SV_POSITION_C_ID
This command will cause the receiver to continuously emit sv positions for all channels. Set flag to '1' to turn streaming on, '0' for off.

### SET_ACQ_CONFIG_C_ID
This command allows the user to customize the acquisition process. The min_doppler and max_doppler arguments define the upper and lower bounds of the Doppler search space. Note that if these lie outside the #define MAX_DOPPLER found in config.h they will be set to MAX_DOPPLER. The doppler_range argument defines the Doppler search space, plus-minus, to search over if the receiver has state information and the almanac is decoded for the given SV (i.e. a warm acquisition).

The last three arguments allow control of the strong, medium, and weak acquisition modes. A value of '0' turns the particular mode off completely. A value of '1' turns the mode on for both cold and warm acquisitions. Finally a value of '2' allows the receiver to search in the given mode only for a warm acquisition.

### SET_PVT_C_ID
This command initializes the receiver's PVT solution with the included state information. If the receiver also has a current almanac this enables a narrowing of the search space and facilitates faster acquisition of signals.

# Messages
## Overview
Messages are one of three types: fixed, requestable, and streaming.

Fixed messages will be emitted by the receiver after each PVT solution generation. Fixed messages CANNOT be turned off.

Requestable messages will be emitted by the receiver only after receiver is given a command to do so. They will be emitted only once for each command received.

Streaming messages have the ability to be turned on and off as required. These messages are typically data that can be used to debug the internal workings of the receiver. If activated, these messages will be emitted at the same rate as the periodic messages, i.e. once per PVT solution.

Finally, the COMMAND_M_ID and COMMAND_ACK_M_ID are special cases. The receiver requires a valid telecommand packet to have the APID filled with the COMMAND_M_ID. This packet type will never be transmitted by the receiver. Upon the successful reception and execution of a command a COMMAND_ACK_M_ID packet will be emitted by the receiver. The payload of this packet will include the receiver's command count and the ID of the executed command.

## Message APID & Type Map

Command	Application Process Identifier	Type
COMMAND_M_ID	1	N/A
COMMAND_ACK_M_ID	2	N/A
TASK_HEALTH_M_ID	3	Fixed
SPS_M_ID	4	Fixed
CLOCK_M_ID	5	Fixed
EKF_M_ID	6	Fixed
CHANNEL_M_ID	7	Streaming
SV_POSITION_M_ID	8	Streaming
MEASUREMENT_M_ID	9	Streaming
PSEUDORANGE_M_ID	10	Streaming
EPHEMERIS_M_ID	11	Request
ALMANAC_M_ID	12	Request
EPHEMERIS_VALID_M_ID	13	Request
SV_PREDICTION_M_ID	14	Request
ACQ_COMMAND_M_ID	15	Request
ACQ_CONFIG_M_ID	16	Request
BOARD_HEALTH_M_ID	17	Request
	18
	19
	20
	21
	22
	23
	24
	25
	26
	27

## Message Descriptors
### COMMAND_M_ID
This is a special packet type. The receiver expects commands to have this APID. This message should never be emitted by the receiver. Additionally, there is no associated structure for this APID.

### COMMAND_ACK_M_ID
This message will be sent upon completion of each command sent to the receiver. The command_status will indicate success or a rejection of the command.

### TASK_HEALTH_M_ID
This message contains the execution counters, OS start tic, and OS stop tic of each thread's main body of code. The least significant bit of the start and stop tics correspond to a 10 millisecond duration. The tasks will be identified by the enum TASK_IDS found in config.h.

### SPS_M_ID
The single point solution (SPS) message is the main output of the receiver. It gives the receiver's estimated position, velocity, acceleration, and time based on the least squares algorithm. The SPS will be updated only when >4 SVs are being concurrently tracked.

### CLOCK_M_ID
The clock message gives more detailed information concerning the receiver's estimate of time, based on the least squares PVT.
### CHANNEL_M_ID
The channel message gives detailed insight into the status of each tracking channel.

### SV_POSITION_M_ID
The SV position message gives information on the calculated SV position based on the GPS ephemeris. This position will correspond to the time of transmission, per IS-GPS-200D. The SV position will be updated each time the receiver computes a least squares PVT solution.

### EKF_M_ID
Currently the extended Kalman filter does not exist in the receiver, this structure will change when it is added.

### MEASUREMENT_M_ID
The measurement message gives the raw correlator state taken at each measurement tic. This measurement is turned into a pseudorange in the PVT thread.

### PSEUDORANGE_M_ID
The pseudorange message contains the raw pseudorange calculated by the receiver when forming the PVT solution.

### BOARD_HEALTH_M_ID
This message provides status and health concerning the receiver's hardware, including portions of the RF card, power supply voltages, thermistor readings, and FPGA version registers.

### EPHEMERIS_M_ID
The decoded ephemeris, read IS-GPS-200D for more specific information.

### ALMANAC_M_ID
The decoded almanac, read IS-GPS-200D for more specific information.

### EPHEMERIS_VALID_M_ID
Provides insight into the status of the Ephemeris object, indicating which ephemerides and almanacs have been decoded.

### SV_PREDICTION_M_ID
The predicted state of the given SV. This information is updated in the SV_Select thread using the PVT's output and the almanac.

### ACQ_COMMAND_M_ID
This message gives insight into the acquisition engine's most recent acquisition attempt.