GPS-SDR

Software Interface Specification

Revision 1.0

October 9, 2008

NASA Goddard Space Flight Center
Greenbelt, MD 20771

Revision History

Revision/Change Record
Revision	Date	Description	Pages Affected
1	10/27/08	Initial Release	All

# Introduction

This document describes the command and telemetry interface for the gps-sdr receiver. Users may use the provided GUI (gps-gui) to control the receiver in an interactive manner, or can use the information in this document to directly apply commands to the receiver over the named pipe or RS-232 interface.

# GPS-SDR Command Arguments

The following descriptions can be accessed by typing “gps-sdr –help” at the command line:

usage: [-p] [-c] [-l] [-d] [-g] [-v] [-n] [-gui] [-ser] [-w] [-u]
[-p] <filename> use prerecorded data
[-c] log high rate channel data
[-l] log navigation data
[-d] <N> decimate logged nav data by this N factor
[-g] log google earth data
[-v] be verbose
[-n] ncurses OFF
[-gui] run receiver with the GUI app over a named pipe
[-ser] run receiver with the GUI app over a serial port
[-w] start receiver in warm start, using almanac and last good position
[-u] run receiver with usrp-gps as child process

# GPS-SDR Interfaces

The gps-sdr is able to utilize two interfaces, a named pipe interface for control on the same computer that the receiver is running, or over a RS-232 serial connection. Only one may be used at any given time. The named pipe (NP) interface provides more flexibility, mainly because it is not bandwidth limited. The RS-232 connection operates at 115200 bps, limiting the telemetry bandwidth to ~14 KB/s.

The named pipe interface is composed of two Linux named pipes, one for sending commands to the receiver, and the other for telemetry output:

Receiver input:	/tmp/GUI2GPS
Receiver output:	/tmp/GPS2GUI

To start the receiver using this interface run the following command:

gps-sdr -gui

The receiver, by default, will send data out at a rate of 10 Hz. This can be lowered by using the “-d” command argument on startup. Use “-d” command in the following manner:

[-d] <N> decimate logged nav data by this N factor

Note N should be a factor of TICS_PER_SECOND found in config.h. By default TICS_PER_SECOND == 10, hence N can be 1, 2, 4, 5, or 10.

The RS-232 interface will use /dev/ttyS0 configured in the following manner:

Baud	115200
Parity	None
Stop Bits	1
Data Bits	8
Flow Control	None

Note that the user should limit the telemetry to 1 Hz, so the flag “-d 10” should be used in conjuction with “-ser”. To start the receiver in serial mode, use the command:

gps-sdr -ser -d 10
# Packets

GPS-SDR uses CCSDS packet headers for both the command and telemetry packets. Additionally, packets are limited to 512 bytes TOTAL (i.e. including the 12 byte CCSDS header). Larger messages and commands will be broken into subpackets, with the appropriate CCSDS header configuration. The CCSDS packet description can be found at:

http://public.ccsds.org/publications/archive/133x0b1.pdf
# Commands

The code that corresponds with the following descriptors can be found in commands.h, which describes the command structures, and in commando.h and commando.cpp, which implements the command functionality. The commands are identified by an enum found in commands.h. Internally the commands will be zero indexed, with the dummy command FIRST_C_ID taking the 0th command, and the command LAST_C_ID occupying the final command. The union Union_C will hold all the defined and implemented commands. All commands and structures are 4 byte aligned! Note, as a rule, command and telemetry structures will only use the following types:

Type	Description
int32	32 bit signed integer
uint32	32 bit unsigned integer
float	32 bit floating point
double	64 bit floating point

## RESET_PVT_C_ID
typedef struct Reset_PVT_C
{
uint32 flag;	//!< Flag for no reason
} Reset_PVT_C;

This command resets the receiver's single point position (PVT) to the center of the earth, and erases all knowledge of GPS time. The argument flag is not used.

## RESET_EKF_C_ID
typedef struct Reset_EKF_C
{
uint32 flag;	//!< Flag for no reason
} Reset_EKF_C;

This command resets the receiver's extend Kalman filter state to the center of the earth, and erases all knowledge of GPS time withing the EKF. Note the EKF will not reinitialize until the receiver produces 60 consecutive valid PVT solutions.

## RESET_CHANNEL_C_ID
typedef struct Reset_Channel_C
{
int32 chan;	//!< Channel #, or all if chan > MAX_CHANNELS
} Reset_Channel_C;

This command has the receiver dump the given tracking channel. This command can be useful if a cross correlation is detected by the user but the receiver has not rejected it. Note that the argument chan is ZERO indexed, hence valid values range from 0 to the #define MAX_CHANNELS found in config.h. If chan is a non-valid value the receiver will reset ALL the channels.

## RESET_EPHEMERIS_C_ID
typedef struct Reset_Ephemeris_C
{
int32 sv;	//!< SV #, or all if sv > NUM_CODES
} Reset_Ephemeris_C;

The command will cause the receiver to erase knowledge of the given SV's decoded ephemeris. If SV > NUM_CODES or < 0, then ALL ephemerides will be erased.

## RESET_ALMANAC_C_ID
typedef struct Reset_Almanac_C
{
int32 sv;	//!< SV #, or all if sv > NUM_CODES
} Reset_Almanac_C;

The command will cause the receiver to erase knowledge of the given SV's decoded almanac. If SV > NUM_CODES or < 0, then ALL almanacs will be erased.

## GET_MEASUREMENT_C_ID
typedef struct Get_Measurement_C
{
int32 chan;	//!< Channel #, or all if chan > MAX_CHANNELS
} Get_Measurement_C;

This command will cause the receiver to continuously emit raw measurements corresponding to the given channel. Again the channel number is ZERO indexed. If chan >= MAX_CHANNELS then ALL channels will be emitted. If chan < 0, then the measurements will no longer be output.
## GET_PSEUDORANGE_C_ID
typedef struct Get_Pseudorange_C
{
int32 chan;	//!< Channel #, or all if chan > MAX_CHANNELS
} Get_Pseudorange_C;

This command will cause the receiver to continuously emit pseudoranges corresponding to the given channel. Again the channel number is ZERO indexed. If chan >= MAX_CHANNELS then ALL channels will be emitted. If chan < 0, then the pseudoranges will no longer be output.

## GET_EPHEMERIS_C_ID
typedef struct Get_Ephemeris_C
{
int32 sv;	//!< SV #, or all if sv >= NUM_CODES || sv < 0
} Get_Ephemeris_C;

This will cause the receiver to emit the given SV's decoded ephemeris. If SV < 0 || SV >= NUM_CODES then all ephemerides will be emitted.

## GET_ALMANAC_C_ID
typedef struct Get_Almanac_C
{
int32 sv;	//!< SV #, or all if sv >= NUM_CODES || sv < 0
} Get_Almanac_C;

This will cause the receiver to emit the given SV's decoded almanac. If SV < 0 || SV >= NUM_CODES then all almanacs will be emitted.

## SET_ALMANAC_C_ID
typedef struct Set_Almanac_C
{
int32 sv;	//!< SV #
Almanac_M almanac;	//!< Data to load
} Set_Almanac_C;

This command allow the external loading of the almanac. The command will simply copy the Almanac_M held in almanac to the SV enumerated in the argument sv. Note that sv must be >=0 & < NUM_CODES, else the command will be ignored.

## SET_EPHEMERIS_C_ID
typedef struct Set_Ephemeris_C
{
int32 sv;	//!< SV #
Ephemeris_M ephemeris;	//!< Data to load
} Set_Ephemeris_C;

This command allow the external loading of the ephmerides. The command will simply copy the Ehpemeris_M held in ephemeris to the SV enumerated in the argument sv. Note that sv must be >=0 & < NUM_CODES, else the command will be ignored.

# Messages

The code that corresponds with the following descriptors can be found in messages.h, which describes the command structures, and in serial_telemetry.h and serial_telemetry.cpp, which implements the telemetry functionality. The messages are identified by an enum found in messages.h. Internally the messages will be zero indexed, with the dummy command FIRST_M_ID taking the 0th messages, and the command LAST_M_ID occupying the final messages. The union Union_M will hold all the defined and implemented messages. All messages and structures are 4 byte aligned. Note, as a rule, command and telemetry structures will only use the following types:

Type	Description
int32	32 bit signed integer
uint32	32 bit unsigned integer
float	32 bit floating point
double	64 bit floating point