GPS-SDR

Interface Specification

Revision 1.0

October 9, 2008

Revision History

Revision/Change Record
Revision	Date	Description	Pages Affected
1	10/27/08	Initial Release	All

# Introduction

This document describes the command and telemetry interface for the gps-sdr receiver. Users may use the provided GUI (gps-gui) to control the receiver in an interactive manner, or can use the information in this document to directly apply commands to the receiver over the named pipe or RS-232 interface.

# GPS-SDR Command Arguments

The following descriptions can be accessed by typing “gps-sdr –help” at the command line:

usage: [-p] [-c] [-l] [-d] [-g] [-v] [-n] [-gui] [-ser] [-w] [-u]
[-p] <filename> use prerecorded data
[-c] log high rate channel data
[-l] log navigation data
[-d] <N> decimate logged nav data by this N factor
[-g] log google earth data
[-v] be verbose
[-n] ncurses OFF
[-gui] run receiver with the GUI app over a named pipe
[-ser] run receiver with the GUI app over a serial port
[-w] start receiver in warm start, using almanac and last good position
[-u] run receiver with usrp-gps as child process

# GPS-SDR Physical Interfaces

The gps-sdr is able to utilize two interfaces, a named pipe interface for control on the same computer that the receiver is running, or over a RS-232 serial connection. Only one may be used at any given time. The named pipe (NP) interface provides more flexibility, mainly because it is not bandwidth limited. The RS-232 connection operates at 115200 bps, limiting the telemetry bandwidth to ~14 KB/s.

The named pipe interface is composed of two Linux named pipes, one for sending commands to the receiver, and the other for telemetry output:

Receiver input:	/tmp/GUI2GPS
Receiver output:	/tmp/GPS2GUI

To start the receiver using this interface run the following command:

gps-sdr -gui

The receiver, by default, will send data out at a rate of 10 Hz. This can be lowered by using the “-d” command argument on startup. Use “-d” command in the following manner:

[-d] <N> decimate logged nav data by this N factor

Note N should be a factor of TICS_PER_SECOND found in config.h. By default TICS_PER_SECOND == 10, hence N can be 1, 2, 4, 5, or 10.

The RS-232 interface will use /dev/ttyS0 configured in the following manner:

Baud	115200
Parity	None
Stop Bits	1
Data Bits	8
Flow Control	None

Note that the user should limit the telemetry to 1 Hz, so the flag “-d 10” should be used in conjunction with “-ser”. To start the receiver in serial mode, use the command:

gps-sdr -ser -d 10

# Packets

GPS-SDR uses packet headers, defined by the Consultative Committee for Space Data Systems (CCSDS), for both the command and telemetry packets. Each packet, composed of the preamble, header, and payload, will be limited to 512 bytes TOTAL. Larger messages and commands will be broken into subpackets, with the appropriate CCSDS header configuration. The CCSDS packet header description can be found at:

http://public.ccsds.org/publications/archive/133x0b1.pdf

The packet format is illustrated below:

Preamble

0xAAAA
0xAAAA

32 bits
Packet
Version
Number

3 bits
Packet
Type

1 bit
Sec.
Hdr.
Flag

1 bit
Application
Process
Identifier

11 bits
Packet Identification
Sequence
Flags

2 bits
Packet
Sequence
Count

14 bits
Packet
Data
Length

16 bits
Packet Sequence Control

Payload

Up to 496 bytes

The preamble will always be 0xAAAAAAAA (alternating 1's and 0's). The packet version number, as recommended in CCSDS 133.0-B-1, will be '000'. The packet type will be '0' for messages, and '1' for commands. The secondary header flag will always be '0', given that the secondary CCSDS header will NOT be used.

The sequence flag will follow the format described in CCSDS 133.0-B-1 to indicate messages broken over multiple packets. The sequence count will contain the least significant 14 bits of the receiver's internal count of the number of packets it has emitted. Finally the packet length will contain the number of bytes in the payload. Given the packet's size limit of 512 bytes, this value can be as large as 496 bytes. The payload will be filled by the structure corresponding to the APID. The mnemonics linking APID, enum, structure, and variable are as follows:

Enum	NAME_M_ID or NAME_C_ID
Structure	Name_M or NAME_C
Variable	name

All commands and structures must be 4 byte aligned. Note, as a rule, command and telemetry structures will only use the following types for data members:

Type	Description
int32	32 bit signed integer
uint32	32 bit unsigned integer
float	32 bit floating point
double	64 bit floating point

Smaller values (16 bit or 8 bit) may be accessed by explicit packing of the data members. Any data members that are packed will be described thouroughly in this document.

# Commands
## RESET_PVT_C_ID
typedef struct Reset_PVT_C
{
uint32 flag;	//!< Flag for no reason
} Reset_PVT_C;

This command resets the receiver's single point position (PVT) to the center of the earth, and erases all knowledge of GPS time. The argument flag is not used.

## RESET_EKF_C_ID
typedef struct Reset_EKF_C
{
uint32 flag;	//!< Flag for no reason
} Reset_EKF_C;

This command resets the receiver's extend Kalman filter state to the center of the earth, and erases all knowledge of GPS time within the EKF. Note the EKF will not reinitialize until the receiver produces 60 consecutive valid PVT solutions.

## RESET_CHANNEL_C_ID
typedef struct Reset_Channel_C
{
int32 chan;	//!< Channel #, or all if chan > MAX_CHANNELS
} Reset_Channel_C;

This command has the receiver dump the given tracking channel. This command can be useful if a cross correlation is detected by the user but the receiver has not rejected it. Note that the argument chan is ZERO indexed, hence valid values range from 0 to the #define MAX_CHANNELS found in config.h. If chan is a non-valid value the receiver will reset ALL the channels.

## RESET_EPHEMERIS_C_ID
typedef struct Reset_Ephemeris_C
{
int32 sv;	//!< SV #, or all if sv > NUM_CODES
} Reset_Ephemeris_C;

The command will cause the receiver to erase knowledge of the given SV's decoded ephemeris. If sv > NUM_CODES or < 0, then ALL ephemerides will be erased.

## RESET_ALMANAC_C_ID
typedef struct Reset_Almanac_C
{
int32 sv;	//!< SV #, or all if sv > NUM_CODES
} Reset_Almanac_C;

The command will cause the receiver to erase knowledge of the given SV's decoded almanac. If sv > NUM_CODES or < 0, then ALL almanacs will be erased.

## GET_MEASUREMENT_C_ID
typedef struct Get_Measurement_C
{
int32 chan;	//!< Channel #, or all if chan > MAX_CHANNELS
} Get_Measurement_C;

This command will cause the receiver to continuously emit raw measurements corresponding to the given channel. Again the channel number is ZERO indexed. If chan >= MAX_CHANNELS then ALL channels will be emitted. If chan < 0, then the measurements will no longer be output.
## GET_PSEUDORANGE_C_ID
typedef struct Get_Pseudorange_C
{
int32 chan;	//!< Channel #, or all if chan > MAX_CHANNELS
} Get_Pseudorange_C;

This command will cause the receiver to continuously emit pseudoranges corresponding to the given channel. Again the channel number is ZERO indexed. If chan >= MAX_CHANNELS then ALL channels will be emitted. If chan < 0, then the pseudoranges will no longer be output.

## GET_EPHEMERIS_C_ID
typedef struct Get_Ephemeris_C
{
int32 sv;	//!< SV #, or all if sv >= NUM_CODES || sv < 0
} Get_Ephemeris_C;

This will cause the receiver to emit the given SV's decoded ephemeris.
If sv < 0 || sv >= NUM_CODES then all ephemerides will be emitted.

## GET_ALMANAC_C_ID
typedef struct Get_Almanac_C
{
int32 sv;	//!< SV #, or all if sv >= NUM_CODES || sv < 0
} Get_Almanac_C;

This will cause the receiver to emit the given SV's decoded almanac.
If sv < 0 || sv >= NUM_CODES then all almanacs will be emitted.

## SET_ALMANAC_C_ID
typedef struct Set_Almanac_C
{
int32 sv;	//!< SV #
Almanac_M almanac;	//!< Data to load
} Set_Almanac_C;

This command allows the external loading of the almanac. The command will simply copy the Almanac_M held in almanac to the SV enumerated in the argument sv. Note that sv must be >=0 & < NUM_CODES, else the command will be ignored.

## SET_EPHEMERIS_C_ID
typedef struct Set_Ephemeris_C
{
int32 sv;	//!< SV #
Ephemeris_M ephemeris;	//!< Data to load
} Set_Ephemeris_C;

This command allow the external loading of the ephemerides. The command will simply copy the Ephemeris_M held in ephemeris to the SV enumerated in the argument sv. Note that sv must be >=0 & < NUM_CODES, else the command will be ignored.

## COMMAND BYTEWISE TABLE

Command	Application Process Identifier	Element / Name	Type	Offset	Size
RESET_PVT_C_ID	1	flag	int32	0x0	4

RESET_EKF_C_ID	2	flag	int32	0x0	4

RESET_CHANNEL_C_ID	3	chan	int32	0x0	4

RESET_EPHEMERIS_C_ID	4	sv	int32	0x0	4

RESET_ALMANAC_C_ID	5	sv	int32	0x0	4

GET_MEASUREMENT_C_ID	6	chan	int32	0x0	4

GET_PSEUDORANGE_C_ID	7	chan	int32	0x0	4

GET_EPHEMERIS_C_ID	8	sv	int32	0x0	4

GET_ALMANAC_C_ID	9	sv	int32	0x0	4

SET_ALMANAC_C_ID	10	sv	int32	0x0	4
		almanac	Almanac_M	0x4

SET_EPHEMERIS_C_ID	11	sv	int32	0x0	4
		ephemeris	Ephemeris_M	0x4

ACQ_CONFIG_C_ID	12	min_doppler	int32	0x0	4
		max_doppler	int32	0x4	4
		doppler_range	int32	0x8	4
		acq_strong	int32	0xC	4
		acq_medium	int32	0x10	4
		acq_weak	int32	0x14	4

CLOCK_CONFIG_C_ID	13	week	double	0x0	8
		second	double	0x8	8

# Messages

Messages are one of three types: periodic, requestable, and streaming.

Periodic messages will be emitted by the receiver after each PVT solution generation, which is tied to the measurement interrupt. Periodic message CANNOT be turned off, the receiver will emit these messages as long as it is active.

Requestable messages will be emitted by the receiver only after receiver receives a command to do so. They will be emitted only once for each command received.

Streaming messsages have the ability to be turned on and off as required. These messages are typically data that can be used to debug the internal workings of the receiver. If activated, these messages will be emitted at the same rate as the periodic messages, namely once per measurement interrupt.

Message	Type
BOARD_HEALTH_M_ID	Request
TASK_HEALTH_M_ID	Periodic
CHANNEL_HEALTH_M_ID	Periodic
SPS_M_ID	Periodic
CLOCK_M_ID	Periodic
SV_POSITION_M_ID	Streaming
EKF_M_ID	Periodic
MEASUREMENT_M_ID	Streaming
PSEUDORANGE_M_ID	Streaming
EPHEMERIS_M_ID	Request
ALMANAC_M_ID	Request
EPHEMERIS_VALID_M_ID	Streaming
COMMAND_ACK_M_ID	Request
SV_PREDICTION_M_ID	Request
ACQ_COMMAND_M_ID	Streaming

## BOARD_HEALTH_M_ID
typedef struct Board_Health_M
{
uint32 trk_version;	//!< Tracking FPGA version
uint32 acq_version;	//!< Acquisition FPGA version
uint32 dsa0;	//!< Current state of DSA 0
uint32 dsa1;	//!< Current state of DSA 1
uint32 dsa2;	//!< Current state of DSA 2
uint32 dsa3;	//!< Current state of DSA 3
uint32 ovrflw0;	//!< Overflow counter on A/D 0
uint32 ovrflw1;	//!< Overflow counter on A/D 1
uint32 ovrflw2;	//!< Overflow counter on A/D 2
uint32 ovrflw3;	//!< Overflow counter on A/D 3
uint32 lo_locked;	//!< Is the LO locked to the synthesizer
uint32 sram_bad_mem;	//!< Debug info from Steve's POST
uint32 sram_bad_hi;	//!< Debug info from Steve's POST
uint32 sram_bad_lo;	//!< Debug info from Steve's POST
uint32 missed_interrupts;	//!< Missed interrupts
uint32 software_major;	//!< Major version
uint32 software_minor;	//!< Minor version
uint32 software_postfix;	//!< Alpha, beta, or gold
} Board_Health_M;

This message provides status and health concerning the receiver's hardware, including portions of the RF card, power supply voltages, thermistor readings, and FPGA version registers.

## TASK_HEALTH_M_ID
typedef struct Task_Health_M
{
uint32 execution_tic[MAX_TASKS];	//!< Execution counters
uint32 start_tic[MAX_TASKS];	//!< Nucleus tic at function entry
uint32 stop_tic[MAX_TASKS];	//!< Nucleus tic at function exit
} Task_Health_M;

This message contains the execution counters, OS start tic, and OS stop tic of each thread's main body of code. The least significant bit of the start and stop tics correspond to a 10 millisecond duration. The tasks will be identified by the enum TASK_IDS found in config.h.

## CHANNEL_HEALTH_M_ID
typedef struct Channel_Health_M
{
float chan;	//!< The channel number
float state;	//!< channel's state
float sv;	//!< SV/PRN number the channel is tracking
float antenna;	//!< Antenna channel is tracking off of
float len;	//!< acummulation length (1 or 20 ms)
float w;	//!< 3rd order PLL state
float x;	//!< 3rd order PLL state
float z;	//!< 3rd order PLL state
float code_nco;	//!< State of code_nco
float carrier_nco;	//!< State of carrier_nco
float CN0;	//!< CN0 estimate
float p_avg;	//!< Filtered version of I^2+Q^2
float bit_lock;	//!< Bit lock?
float frame_lock;	//!< Frame lock?
float navigate;	//!< Navigate on this channel flag
float count;	//!< Number of accumulations that have been processed
float subframe;	//!< Current subframe number
float best_epoch;	//!< Best estimate of bit edge position
} Channel_Health_M;

The channel health message gives insight into the status of each tracking channel.

## SPS_M_ID
typedef struct SPS_M
 {
double x;	//!< ECEF x coordinate (meters)
double y;	//!< ECEF y coordinate (meters)
double z;	//!< ECEF z coordinate (meters)
double vx;	//!< ECEF x velocity (meters/sec)
double vy;	//!< ECEF x velocity (meters/sec)
double vz;	//!< ECEF x velocity (meters/sec)
double ax;	//!< ECEF x acceleration (meters/sec/sec)
double ay;	//!< ECEF x acceleration (meters/sec/sec)
double az;	//!< ECEF x acceleration (meters/sec/sec)
double time;	//!< time in seconds
double clock_bias;	//!< clock bias in seconds
double clock_rate;	//!< clock rate in meters/second
double latitude;	//!< latitude in decimal radians
double longitude;	//!< longitude in decimal radians
double altitude;	//!< height in meters
double gdop;	//!< geometric dilution of precision
double pdop;	//!< position dilution of precision
double tdop;	//!< time dilution of precision
double hdop;	//!< horizontal dilution of precision
double vdop;	//!< vertical dilution of precision
uint32 nsvs;	//!< This is a mask, not a number
uint32 converged;	//!< declare convergence
uint32 tic;	//!< global_tic associated with this solution
uint32 stale_ticks;//!< count the number of ticks since the last good sltn
uint32 converged_ticks;	//!< count number of converged ticks
uint32 nav_channels;	//!< count number of SVs used in last PVT estimation
uint32 initial_convergence;	//!< Flag set ONCE if the first convergence has occured

uint32 chanmap[MAX_CHANNELS]; //!< Map of channels->sv
} SPS_M;

The single point solution (SPS) message is the main output of the receiver. It gives the receiver's estimated position, velocity, acceleration, and time based on the least squares algorithm. The SPS will be updated only when >4 SVs are being concurrently tracked, else the position will remain static apart from the variables tic, stale_ticks, chanmap, and nav_channels.

## CLOCK_M_ID
typedef struct Clock_M
{
double receiver_time;	//!< Elapsed receiver time
double rate;	//!< Clock rate
double bias;	//!< Clock bias
double time0;	//!< Guess of gps second at initialization
double time;	//!< Best estimate of GPStime
double time_raw;	//!< Uncorrected time
double week;	//!< GPS week
uint32 state;	//!< Clock state
} Clock_M;

The clock message gives more detailed information concerning the receiver's estimate of time, based on the least squares PVT.

## SV_POSITION_M_ID
typedef struct SV_Position_M
{
double x;	//!< ECEF x coordinate (meters)
double y;	//!< ECEF y coordinate (meters)
double z;	//!< ECEF z coordinate (meters)
double vx;	//!< ECEF x velocity (meters/sec)
double vy;	//!< ECEF x velocity (meters/sec)
double vz;	//!< ECEF x velocity (meters/sec)
double ax;	//!< ECEF x acceleration (meters/sec/sec)
double ay;	//!< ECEF x acceleration (meters/sec/sec)
double az;	//!< ECEF x acceleration (meters/sec/sec)
double elev;	//!< Satellite elevation (radians)
double azim;	//!< Satellite azimuth (radians)
double clock_bias;	//!< SV clock bias (seconds)
double frequency_bias;	//!< SV clock rate bias (seconds/second)
double transit_time;	//!< Time of flight from SV to receiver (seconds)
double time;	//!< Time used in SV position calculation (seconds)
double latitude;	//!< Latitude using WGS-84 ellipsoid in decimal (radians)
double longitude;	//!< Longitude using WGS-84 ellipsoid in decimal (radians)
double altitude;	//!< height (meters)
uint32 chan;	//!< Corresponding channel
} SV_Position_M;

The SV position message gives information on the calculated SV position based on the GPS ephemeris. This position will correspond to the time of transmission, per IS-GPS-200D. The SV position will be updated each time the receiver computes a least squares PVT solution.

## EKF_M_ID
typedef struct EKF_M
{
double x;	//!< ECEF x coordinate (meters)
double y;	//!< ECEF y coordinate (meters)
double z;	//!< ECEF z coordinate (meters)
double vx;	//!< ECEF x velocity (meters/sec)
double vy;	//!< ECEF x velocity (meters/sec)
double vz;	//!< ECEF x velocity (meters/sec)
double ax;	//!< ECEF x acceleration (meters/sec/sec)
double ay;	//!< ECEF x acceleration (meters/sec/sec)
double az;	//!< ECEF x acceleration (meters/sec/sec)
double time;	//!< time in seconds
double clock_bias;	//!< clock bias in seconds
double clock_rate;	//!< clock rate in meters/second
double latitude;	//!< latitude in decimal radians
double longitude;	//!< longitude in decimal radians
double altitude;	//!< height in meters
double gdop;	//!< geometric dilution of precision
double pdop;	//!< position dilution of precision
double tdop;	//!< time dilution of precision
double hdop;	//!< hdop diultion of precision
double vdop;	//!< vertical dilution of precision
uint32 nsvs;	//!< This is a mask, not a number
uint32 converged;	//!< declare convergence
uint32 tic;	//!< global_tic associated with this solution
uint32 stale_ticks;	//!< count the number of tics since the last good sltn
uint32 converged_ticks;	//!< count number of converged tics
uint32 nav_channels;	//!< count number of SVs used in last PVT estimation
uint32 initial_convergence;	//!< Flag set ONCE if the first convergence has occured

uint32 chanmap[MAX_CHANNELS];
} EKF_M;

Currently the extended Kalman filter does not exist in the receiver, this structure will change when it is added.

## MEASUREMENT_M_ID
typedef struct Measurement_M
{
double code_time;	//!< The code time
double code_phase;	//!< Code phase (chips)
double carrier_phase;	//!< Carrier phase (cycles)
double carrier_phase_prev;	//!< Carrier phase prev (cycles)
double carrier_phase_prev_prev;//!< Carrier phase prev prev (cycles)
double code_phase_mod;	//!< Code phase (chips), mod 1023
double carrier_phase_mod;	//!< Carrier phase (cycles), mod 1
double code_nco;	//!< Code NCO
double carrier_nco;	//!< Carrier NCO
uint32 _1ms_epoch;	//!< _1ms_epoch
uint32 _20ms_epoch;	//!< _20ms_epoch
uint32 _z_count;	//!< The z count
uint32 navigate;	//!< This has been tagged as a good measurement
uint32 sv;	//!< For this sv
uint32 chan;	//!< For this channel
uint32 count;	//!< Corresponds to this tic
} Measurement_M;

The measurement message gives the raw correlator state taken at each measurement tic. This measurement is turned into a pseudorange in the PVT thread.

## PSEUDORANGE_M_ID
typedef struct Pseudorange_M
{
double gpstime;	//!< Time tag associated with pseudorange
double time;	//!< pseudorange in seconds
double time_rate;	//!< pseudorange rate in sec/sec
double meters;	//!< pseudorange in meters
double meters_rate;	//!< pseudorange rate in meters/sec
double residual;	//!< residual in meters
double rate_residual;	//!< rate residual (m/s)
double time_uncorrected;	//!< raw pseudorange measurements
double previous;	//!< from previous step, used for err check
uint32 chan;	//!< For this channel
uint32 count;	//!< Corresponds to this tic
} Pseudorange_M;

The pseudorange message contains the raw pseudorange calculated by the receiver when forming the PVT solution.

## EPHEMERIS_M_ID
typedef struct Ephemeris_M
{
double tgd;	//!< Group delay parameter.
double toc;	//!< Reference time of clock data parameter set.
double af0;	//!< Clock correction polynomial coefficient.
double af1;	//!< Clock correction polynomial coefficient.
double af2;	//!< Clock correction polynomial coefficient.
double crs;	//!< Sine harmonic correction to orbital radius.
double deltan;	//!< Mean motion delta from computed value.
double m0;	//!< Mean anomaly at TOE.
double cuc;	//!< Cosine harmonic correction to orbital radius.
double ecc;	//!< Eccentricity.
double cus;	//!< Sine harmonic corr to argument of latitude.
double sqrta;	//!< Square root of semimajor axis.
double toe;	//!< Reference time of ephemeris data set.
double cic;	//!< Cosine harmonic corr to inclination.
double om0;	//!< Right ascension at TOE.
double cis;	//!< Sine harmonic corr to inclination.
double in0;	//!< Inclination at TOE.
double crc;	//!< Cosine harmonic correction to orbital radius.
double argp;	//!< Argument of perigee at TOE.
double omd;	//!< Rate of right ascension.
double idot;	//!< Rate of inclination.
double a;	//!< Derived qty: a = sqrta**2.
double n0;	//!< Derived qty: n0 = sqrt(GravConstant/(a*a*a)).
double relativistic;	//!< Relativistic correction
uint32 sv;	//!< SV #
uint32 zcount;	//!< zcount?
uint32 toewk;	//!< GPS week corresponding to toe.
uint32 fti;	//!< Fit interval.
uint32 iode;	//!< Issue of data, ephemeris.
uint32 tocwk;	//!< GPS week corresponding to toc.
uint32 valid;	//!< 0=No valid data.
uint32 tofxmission;	//!< Time of subframe 1 transmission, sec of week.
uint32 tow;	//!< Truncated TOW count
uint32 subframe_1_health;	//!< Subframe 1 health code.
uint32 code_on_L2;	//!< Code on L2 flag.
uint32 week_number;	//!< GPS week at time of subframe 1 reception.
uint32 L2pdata;	//!< L2 P data flag.
uint32 ura;	//!< Satellite's URA code.
uint32 iodc;	//!< Issue of data, clock.
} Ephemeris_M;

The decoded ephemeris, read IS-GPS-200D for more specific information.

## ALMANAC_M_ID
typedef struct Almanac_M
{
double ecc;	//!< Eccentricity
double toa;	//!< Time of Almanac
double in0;	//!< Inclination
double omd;	//!< Rate of right ascention
double sqrta;	//!< Sqrt of Semi-Major Axis
double om0;	//!< Longitude of Ascending Node
double argp;	//!< Argument of perigee
double m0;	//!< Mean Anomaly
double af0;	//!< Clock parameter 0
double af1;	//!< Clock parameter 1
uint32 sv;	//!< SV #
uint32 week;	//!< Week number
uint32 decoded;	//!< Has this been decoded yet
uint32 health;	//!< Health code
} Almanac_M;

The decoded almanac, read IS-GPS-200D for more specific information.

## EPHEMERIS_VALID_M_ID
typedef struct Ephemeris_Status_M
{
uint32 valid[NUM_CODES];	//!< Valid ephemeris
uint32 iode[NUM_CODES];	//!< Corresponding IODE
uint32 avalid[NUM_CODES];	//!< Valid almanac
} Ephemeris_Status_M;

Provides insight into the status of the Ephemeris object, indicating which ephemerides and almanacs have been decoded.
## COMMAND_ACK_M_ID
typedef struct Command_Ack_M
{
uint32 command_id;	//!< ID of command received
uint32 command_tic;	//!< Command sequence count
uint32 command_status;	//!< Status (0 for FAIL, 1 for SUCCESS)
} Command_Ack_M;

This message will be sent upon completion of each command sent to the receiver. The command_status will indicate success or a rejection of the command.

## SV_PREDICTION_M_ID
typedef struct _SV_Prediction_M
{
int32 sv;	//!< SV number
int32 visible;	//!< Should the SV be visible?
int32 tracked;	//!< Is it being tracked?
float elev;	//!< Predicted elev (degrees)
float azim;	//!< Predicted azim (degrees)
float v_elev;	//!< Elevation of vehicle relative to SV
float v_azim;	//!< Azimuth of vehicle relative to SV
float delay;	//!< Predicted delay (seconds)
float doppler;	//!< Predicted Doppler (Hz)
float doppler_rate;	//!< Predicted Doppler rate (Hz/sec)
} SV_Prediction_M;

The predicted state of the given SV. This information is updated in the SV_Select thread using the PVT's output and the almanac.

## ACQ_COMMAND_M_ID
typedef struct _Acq_Command_M
{
int32 chan;	//!< Which channel this will be mapped to
int32 sv;	//!< Look for this SV
int32 type;	//!< Type (STRONG/MEDIUM/WEAK)
int32 mindopp;	//!< Minimum Doppler
int32 maxdopp;	//!< Maximum Doppler
int32 antenna;	//!< Antenna number
int32 count;	//!< Packet tag
int32 state;	//!< Request state
int32 success;	//!< Was the SV detected?
float delay;	//!< Delay in chips
float doppler;	//!< Doppler in Hz
float magnitude;	//!< Magnitude
} Acq_Command_M;

This message gives insight into the acquisition engine's status. Each acquisition attempt is emitted by the receiver.

## MESSAGE BYTEWISE TABLE

Command	Element	Type	Offset	Size
BOARD_HEALTH_M_ID	trk_version	uint32	0x0	4
	acq_version	uint32	0x4	4
	dsa0	uint32	0x8	4
	dsa1	uint32	0xC	4
	dsa2	uint32	0x10	4
	dsa3	uint32	0x14	4
	ovrflw0	uint32	0x18	4
	ovrflw1	uint32	0x1C	4
	ovrflw2	uint32	0x20	4
	ovrflw3	uint32	0x24	4
	lo_locked	uint32	0x28	4
	sram_bad_mem	uint32	0x2C	4
	sram_bad_hi	uint32	0x30	4
	sram_bad_lo	uint32	0x34	4
	missed_interrupts	uint32	0x38	4
	software_major	uint32	0x3C	4
	software_minor	uint32	0x40	4
	software_postfix	uint32	0x44	4

TASK_HEALTH_M_ID	execution_tic	uint32	0x0	128
	start_tic	uint32	0x80	128
	stop_tic	uint32	0x100	128

The application process identifier (APID) will be linked to two enums found in commands.h and messages.h. For commands the relevant enum is CCSDS_COMMAND_IDS, for messages CCSDS_MESSAGES_IDS. Externally the application process identifier will be equal to the command or message enum, plus the #define CCSDS_APID_BASE:

Message APID = CCSDS_MESSAGES_IDS(Message type) + CCSDS_APID_BASE + MESSAGE_APID_OFFSET;
Command APID = CCSDS_COMMANDS_IDS(Command type) + CCSDS_APID_BASE + COMMAND_APID_OFFSET;

CCSDS_COMMAND_IDS and CCSDS_MESSAGES_IDS will contain two dummy enumerations in the first and last place:

/* Enum the packet ID #s */	/* Enum the command #s */
enum CCSDS_MESSAGES_IDS	enum CCSDS_COMMAND_IDS
{	{
FIRST_M_ID,	FIRST_C_ID,
BOARD_HEALTH_M_ID,	RESET_PVT_C_ID,
…	...
ACQ_COMMAND_M_ID,	CLOCK_CONFIG_C_ID,
LAST_M_ID	LAST_C_ID
};	};

FIRST_M_ID and FIRST_C_ID will take the 0th position, and LAST_M_ID and LAST_C_ID the last. Hence the APID, minus CCSDS_APID_BASE, will always be larger than zero and less than LAST_M_ID or LAST_C_ID.