GPS-SDR

Interface Specification

Revision 1.0

October 9, 2008

Revision History

Revision/Change Record
Revision	Date	Description	Pages Affected
1	10/27/08	Initial Release	All

# Introduction

This document describes the command and telemetry interface for the gps-sdr receiver. Users may use the provided GUI (gps-gui) to control the receiver in an interactive manner, or can use the information in this document to directly apply commands to the receiver over a named pipe or RS-232 interface.

# GPS-SDR Command Arguments

The following descriptions can be accessed by typing “gps-sdr –help” at the command line:

usage: [-p] [-c] [-l] [-d] [-g] [-v] [-n] [-gui] [-ser] [-w] [-u]
[-p] <filename> use prerecorded data
[-c] log high rate channel data
[-l] log navigation data
[-d] <N> decimate logged nav data by this N factor
[-g] log google earth data
[-v] be verbose
[-n] ncurses OFF
[-gui] run receiver with the GUI app over a named pipe
[-ser] run receiver with the GUI app over a serial port
[-w] start receiver in warm start, using almanac and last good position
[-u] run receiver with usrp-gps as child process

# GPS-SDR Physical Interfaces

The gps-sdr is able to utilize two interfaces, a named pipe interface for control on the same computer that the receiver is running, or over a RS-232 serial connection. Only one may be used at any given time. The named pipe (NP) interface provides more flexibility, mainly because it is not bandwidth limited. The RS-232 connection operates at 115200 bps, limiting the telemetry bandwidth to ~14 kB/s.

The named pipe interface is composed of two Linux named pipes, one for sending commands to the receiver, and the other for the receiver's output:

Receiver input:	/tmp/GUI2GPS
Receiver output:	/tmp/GPS2GUI

To start the receiver using this interface run the following command:

gps-sdr -gui

The receiver, by default, will send data out at a rate of 10 Hz. This can be lowered by using the “-d” command argument on startup. Use the “-d” argument in the following manner:

[-d] <N> decimate logged nav data by this N factor

Note N should be a factor of the #define TICS_PER_SECOND found in config.h. By default TICS_PER_SECOND == 10, hence N can be 1, 2, 4, 5, or 10.

By default gps-sdr will use the RS-232 interface mapped to /dev/ttyS0. The serial configuration is the following:

Baud	115200
Parity	None
Stop Bits	1
Data Bits	8
Flow Control	None

Note that the user should limit the telemetry to 1 Hz, so the flag “-d 10” should be used in conjunction with “-ser”. To start the receiver in serial mode, use the command:

gps-sdr -ser -d 10

# Packets

GPS-SDR uses packet headers, defined by the Consultative Committee for Space Data Systems (CCSDS), for both the command and telemetry packets. Each packet, composed of the preamble, header, and payload, will be limited to 512 bytes TOTAL. Larger messages and commands will be broken into subpackets, with the appropriate CCSDS header configuration. The CCSDS packet header description can be found at:

http://public.ccsds.org/publications/archive/133x0b1.pdf

The packet format is illustrated below:

The preamble will always be 0xAAAAAAAA (alternating 1's and 0's). The packet version number, as recommended in CCSDS 133.0-B-1, will be '000'. The packet type will be '0' for messages, and '1' for commands. The secondary header flag will always be '0', given that the secondary CCSDS header will NOT be used.

The sequence flag will follow the format described in CCSDS 133.0-B-1 to indicate messages broken over multiple packets. The sequence count will contain the least significant 14 bits of the receiver's internal count of the number of packets it has emitted. The packet length will contain the number of bytes in the payload. Given the packet's size limit of 512 bytes, this value can be as large as 496 bytes. The payload will be filled with a structure corresponding to the application process identifier (APID). The mnemonics linking APID, enum, structure, and variable are as follows:

Enum	NAME_M_ID or NAME_C_ID
Structure	Name_M or NAME_C
Variable	name

All commands and structures must be 4 byte aligned. Note, as a rule, command and telemetry structures will only use the following types for data members:

Type	Description
int32	32 bit signed integer
uint32	32 bit unsigned integer
float	32 bit floating point
double	64 bit floating point

Smaller values (16 bit or 8 bit) may be accessed by explicit packing and unpacking of the data members. Any data members that are packed will be described explicitly in this document.

# Commands

## RESET_PVT_C_ID
This command resets the receiver's single point position (SPS) to the center of the earth, and erases all knowledge of GPS time. The argument flag is not used.

## RESET_EKF_C_ID
This command resets the receiver's extend Kalman filter (EKF) state to the center of the earth, and erases all knowledge of GPS time within the EKF. Note the EKF will not reinitialize until the receiver produces 60 consecutive valid PVT solutions. The argument flag is not used.

## RESET_CHANNEL_C_ID
This command forces the receiver dump the given tracking channel. This command can be useful if a cross correlation is detected by the user but the receiver has not rejected it. Note that the argument chan is zero indexed. If chan < 0 || chan >= MAX_CHANNELS the receiver will dump ALL the channels.

## RESET_EPHEMERIS_C_ID
The command will cause the receiver to erase knowledge of the given SV's decoded ephemeris. If sv < 0 || sv >= NUM_CODES, then all ephemerides will be erased.

## RESET_ALMANAC_C_ID
The command will cause the receiver to erase knowledge of the given SV's decoded almanac. If sv < 0 || sv >= NUM_CODES, then all almanacs will be erased.

## GET_MEASUREMENT_C_ID
This command will cause the receiver to continuously emit raw measurements corresponding to the given channel. The channel number is zero indexed. If chan >= MAX_CHANNELS then ALL channels will be emitted. If chan < 0, then the measurements will no longer be output.

## GET_PSEUDORANGE_C_ID
This command will cause the receiver to continuously emit pseudoranges corresponding to the given channel. chan is zero indexed. If chan >= MAX_CHANNELS then ALL channels will be emitted. If chan < 0, then the pseudoranges will no longer be output.
## GET_EPHEMERIS_C_ID
This will cause the receiver to emit the given SV's decoded ephemeris once.
If sv < 0 || sv >= NUM_CODES then all ephemerides will be emitted.

## GET_ALMANAC_C_ID
This will cause the receiver to emit the given SV's decoded almanac once.
If sv < 0 || sv >= NUM_CODES then all almanacs will be emitted.

## SET_ALMANAC_C_ID
This command allows external loading of the almanac. The command will simply copy the Almanac_M held in almanac to the SV enumerated in the argument sv. Note that if
sv < 0 || sv >= NUM_CODES the command will be ignored.

## SET_EPHEMERIS_C_ID
This command allows the external loading of the ephemerides. The command will simply copy the Ephemeris_M held in ephemeris to the SV enumerated in the argument sv. Note that if
sv < 0 || sv >= NUM_CODES the command will be ignored.

## ACQ_CONFIG_C_ID
This command allows the user to customize the acquisition process. The min_doppler and max_doppler defines the upper and lower bounds of the Doppler search space. Note that if these lie outside the #define MAX_DOPPLER found in config.h they will be set to MAX_DOPPLER. The doppler_range argument defines the Doppler search space, plus-minus, to search over if the receiver has state information and the almanac is decoded for the given SV (i.e. a warm acquisition).

The last three arguments allow control of the strong, medium, and weak acquisition modes. A value of '0' turns the particular mode off completely. A value of '1' turns the mode on for both cold and warm acquisitions. Finally a value of '2' allows the receiver to search in the given mode only for a warm acquisition.

## WARM_START_C_ID
This command initializes the receiver with the given state information. If the almanac is loaded into the receiver this allows the receiver to exploit the information to aid the acquisition process.

## GET_ACQ_CONFIG_C_ID
Instructs the receiver to emit the acquisition configuration.

## GET_SV_PREDICTION_C_ID
Instructs the receiver to emit the predicted state of the given SV.
If sv < 0 || sv >= NUM_CODES the receiver will emit predictions for all the SVs.

## GET_EPHEMERIS_VALID_C_ID
Emit the ephemeris and almanac validity message, Ephemeris_Valid_M.

## GET_BOARD_HEALTH_C_ID
Emit the board health message Board_Health_M.

## GET_ACQ_COMMAND_C_ID
Emit the acquisition command and result for the given SV. If sv < 0 || sv >= NUM_CODES the receiver will emit predictions for all the SVs.

## COMMAND BYTEWISE TABLE

Command	Application Process Identifier	Element / Name	Type	Offset	Size
RESET_PVT_C_ID	1	flag	int32	0x0	4

RESET_EKF_C_ID	2	flag	int32	0x0	4

RESET_CHANNEL_C_ID	3	chan	int32	0x0	4

RESET_EPHEMERIS_C_ID	4	sv	int32	0x0	4

RESET_ALMANAC_C_ID	5	sv	int32	0x0	4

GET_MEASUREMENT_C_ID	6	chan	int32	0x0	4

GET_PSEUDORANGE_C_ID	7	chan	int32	0x0	4

GET_EPHEMERIS_C_ID	8	sv	int32	0x0	4

GET_ALMANAC_C_ID	9	sv	int32	0x0	4

SET_ALMANAC_C_ID	10	sv	int32	0x0	4
		almanac	Almanac_M	0x4

SET_EPHEMERIS_C_ID	11	sv	int32	0x0	4
		ephemeris	Ephemeris_M	0x4

SET_ACQ_CONFIG_C_ID	12	min_doppler	int32	0x0	4
		max_doppler	int32	0x4	4
		doppler_range	int32	0x8	4
		acq_strong	int32	0xC	4
		acq_medium	int32	0x10	4
		acq_weak	int32	0x14	4

WARM_START_C_ID	13	x	double	0x0	8
		y	double	0x8	8
		z	double	0x10	8
		vx	double	0x18	8
		vy	double	0x20	8
		vz	double	0x28	8
		second	double	0x30	8
		week	double	0x38	8

GET_ACQ_CONFIG_C_ID	14	flag	int32	0x0	4

GET_SV_PREDICTION_C_ID	15	sv	int32	0x0	4

GET_EPHEMERIS_VALID_C_ID	16	flag	int32	0x0	4

GET_BOARD_HEALTH_C_ID	17	flag	int32	0x0	4

GET_ACQ_COMMAND_C_ID	18	sv	int32	0x0	4

# Messages

Messages are one of three types: fixed, requestable, and streaming.

Fixed messages will be emitted by the receiver after each PVT solution generation, which is tied to the measurement interrupt. Fixed messages CANNOT be turned off, the receiver will emit these messages as long as it is active.

Requestable messages will be emitted by the receiver only after receiver receives a command to do so. They will be emitted only once for each command received.

Streaming messages have the ability to be turned on and off as required. These messages are typically data that can be used to debug the internal workings of the receiver. If activated, these messages will be emitted at the same rate as the periodic messages, i.e. once per PVT solution.

Finally, the COMMAND_ACK_M_ID is a special case. This message is only emitted upon execution of a command.

Message	Type
TASK_HEALTH_M_ID	Fixed
CHANNEL_HEALTH_M_ID	Fixed
SPS_M_ID	Fixed
CLOCK_M_ID	Fixed
EKF_M_ID	Fixed

MEASUREMENT_M_ID	Streaming
PSEUDORANGE_M_ID	Streaming
SV_POSITION_M_ID	Streaming

BOARD_HEALTH_M_ID	Request
ACQ_CONFIG_M_ID	Request
SV_PREDICTION_M_ID	Request
EPHEMERIS_M_ID	Request
ALMANAC_M_ID	Request
EPHEMERIS_VALID_M_ID	Request

COMMAND_ACK_M_ID	N/A

## BOARD_HEALTH_M_ID
This message provides status and health concerning the receiver's hardware, including portions of the RF card, power supply voltages, thermistor readings, and FPGA version registers.

## TASK_HEALTH_M_ID
This message contains the execution counters, OS start tic, and OS stop tic of each thread's main body of code. The least significant bit of the start and stop tics correspond to a 10 millisecond duration. The tasks will be identified by the enum TASK_IDS found in config.h.

## CHANNEL_HEALTH_M_ID
The channel health message gives insight into the status of each tracking channel.

## SPS_M_ID
The single point solution (SPS) message is the main output of the receiver. It gives the receiver's estimated position, velocity, acceleration, and time based on the least squares algorithm. The SPS will be updated only when >4 SVs are being concurrently tracked, else the position will remain static apart from the variables tic, stale_ticks, chanmap, and nav_channels.

## CLOCK_M_ID
The clock message gives more detailed information concerning the receiver's estimate of time, based on the least squares PVT.

## SV_POSITION_M_ID
The SV position message gives information on the calculated SV position based on the GPS ephemeris. This position will correspond to the time of transmission, per IS-GPS-200D. The SV position will be updated each time the receiver computes a least squares PVT solution.

## EKF_M_ID
Currently the extended Kalman filter does not exist in the receiver, this structure will change when it is added.

## MEASUREMENT_M_ID
The measurement message gives the raw correlator state taken at each measurement tic. This measurement is turned into a pseudorange in the PVT thread.

## PSEUDORANGE_M_ID
The pseudorange message contains the raw pseudorange calculated by the receiver when forming the PVT solution.

## EPHEMERIS_M_ID
The decoded ephemeris, read IS-GPS-200D for more specific information.

## ALMANAC_M_ID
The decoded almanac, read IS-GPS-200D for more specific information.

## EPHEMERIS_VALID_M_ID
Provides insight into the status of the Ephemeris object, indicating which ephemerides and almanacs have been decoded.

## COMMAND_ACK_M_ID
This message will be sent upon completion of each command sent to the receiver. The command_status will indicate success or a rejection of the command.

## SV_PREDICTION_M_ID
The predicted state of the given SV. This information is updated in the SV_Select thread using the PVT's output and the almanac.

## ACQ_COMMAND_M_ID
This message gives insight into the acquisition engine's status. Each acquisition attempt is emitted by the receiver.

# Appendix 1: Command Structures

# Appendix 2: Message Structures

CCSDS_COMMAND_IDS and CCSDS_MESSAGES_IDS will contain two dummy enumerations in the first and last place:

/* Enum the packet ID #s */	/* Enum the command #s */
enum CCSDS_MESSAGES_IDS	enum CCSDS_COMMAND_IDS
{	{
FIRST_M_ID,	FIRST_C_ID,
BOARD_HEALTH_M_ID,	RESET_PVT_C_ID,
…	...
ACQ_COMMAND_M_ID,	CLOCK_CONFIG_C_ID,
LAST_M_ID	LAST_C_ID
};	};

FIRST_M_ID and FIRST_C_ID will take the 0th position, and LAST_M_ID and LAST_C_ID the last. Hence the APID, minus CCSDS_APID_BASE, will always be larger than zero and less than LAST_M_ID or LAST_C_ID.

#define MOD_ADLER 65521
/* Data is input buffer, len is in bytes! */
uint32 adler(uint8 *data, int32 len)
{

    uint32 a, b;
    int32 tlen;

    a = 1; b = 0;

    if(len < 5552)
    {
        do
        {
        a += *data++;
        b += a;
        } while (--len);

        a %= MOD_ADLER;
        b %= MOD_ADLER;
    }

    return (b << 16) | a;

}